## Slide 1
CYANUS: Calculator for Yield Analysis of NUclear activationS
2022年 4 月 21 日
Tongyuan CUI
矢车菊Centaurea cyanus
灰喜鹊 Cyanopica cyanus
喜鹊 Pica pica

## Slide 2: CYANUS: Calculator for Yield Analysis of Nuclear activationS
Overview
  TINAA aims to provide convenient analytic analysis of delayed gamma rays released from the user defined specimen after nuclear activation.
Inputs:
  One table of the mass of interested elements.
  Spectrum(s) of projectile particle(s)
  Three time period (The irradiation, cooling and measuring time)
Outputs:
  A table containing all possible delayed gamma rays and their counts
  Four tables containing well organized nuclear data showing how to calculate the above table

## Slide 3: Sketch
Element table
Irradiation field
Irradiation, cooling, measurement time
CYANUS
Gamma spectrum
Gamma spectrum for each element

## Slide 4: Sketch
样品构成
辐照场
照射、冷却、测量时长
CYANUS
特征伽马射线总谱
分元素
特征伽马射线谱

## Slide 5: CYANUS: Calculator for Yield Analysis of Nuclear activationS
Features
  Arbitrary energy distribution of projectile particles
  Any elemental constitution is feasible
  Coming: Multiple incident particle, include neutron, gamma, electron
Fields
  Predict the gamma spectrum of certain specimen activated by a specified facility
  Optimize the radiation field for high signal gammas and low background gammas

## Slide 6: Comparison
  MCNP, Geant4
    These codes provide Monte-Carlo simulation of particle transportation and reactions. Typically takes a long time to acquire good statistical error. And the delayed gamma is not considered in these codes.
  Talys
    Talys gives the prediction of nuclear reactions based on nuclear models, but resonance reaction are not modeled, which is important for isotopes have large resonance integration, like Au-197(1550 b), Nd-145 (224 b) and so on.
  K0-IAEA, Kayzero
    They are designed for the deconvolution of the measured gamma spectrum to quantify the elements composition. However, they typically only work for thermal neutrons in the reactor. Since they are for-ward, they do not provide the “prediction” of user defined specimen.
  WISE Uranium Project, FRM II, NCNR
    These online calculator provides a list of neutron activation products of user given elemental composition. However they only provide the activities of isotopes after irradiation, lacks the gamma intensities. Besides, they only works for particular neutron spectrum, lacks the consideration of energy distribution or multiple particles irradiation.
WISE 不提供Ag110m等同质异能态的活化
计算器还有NIST的下面这个
https://www.ncnr.nist.gov/resources/activation/
但它并不提供伽马信息，只提供活度
WISE也只提供活度

## Slide 7: CYANUS basic procedure
Basic modules (matlab functions)
  Cyanus_preparation.m generates 5 structured tables from nuclear data, user defined neutron spectrum and irradiation, cooling, measurement time
  Cyanus_specimen.m fills in the user given elemental composition, then calculate the corresponding info. (Blue)
    Table_element （89 rows，2+1 columns ）
    Table_isotope（287 rows，3+1 columns ）
    Table_active（287 rows，10 columns）
    Table_decay（271rows，6+1 columns）
    Table_gamma（5605 rows，7+1 columns）
Mechanisms
  Organizing (look up the nuclear data or calculate) the parameters in the following activation analysis equation for each possible delayed gamma

## Slide 8: Computation time
  Cyanus_preparation（38 s）
    Table_element (0.6 s)
    Table_isotope (0.6 s)
    Table_active (24 s)
      Numint (10 s)
      Readtable (10 s)
    Table_decay (2.8 s)
      Gethalflife (0.6 s)
    Table_gamma (9.9 s)
  Cyanus_specimen（4 s）
For example:
Analyze 100 ores in 5 different neutron fields:
Total time = 38 s * 5 + 4 s * 5 * 100 = 36 min

## Slide 9: Calculating procedure (Take “In” as example)

## Slide 10: 结构化表格介绍
内容：
稳定元素的原子序数
稳定元素的原子质量
样品中的元素质量
核数据源：
NUBASE2020

## Slide 11: 结构化表格介绍
内容：
稳定元素的原子序数
稳定同位素的核子数
丰度
核素原子核数量
核数据源：
NUBASE2020

## Slide 12: 结构化表格介绍
内容：
稳定元素的原子序数
稳定同位素的核子数
丰度
核素的(n, g)与中子注量积分
到达不同isomer的分支比
核数据源：
ENDF-V8.0 中子俘获截面
TALYS isomeric ratio

## Slide 13: 结构化表格介绍
内容：
长寿命子核列表
长寿命子核核子数
长寿命子核能级
长寿命子核半衰期
产生长寿命子核的注量截面积分
无限长活化得到的子核数
核数据源：
NUBASE2020

## Slide 14: 结构化表格介绍
内容：
长寿命子核列表
长寿命子核核子数
长寿命子核能级
长寿命子核半衰期
产生长寿命子核的注量截面积分
无限长活化得到的子核数
核数据源：
http://nucleardata.nuclear.lu.se/ 缓发伽马能量与分支比

## Slide 15: Integration of neutron spectrum and xs
where
When ，, then

## Slide 16: Integration of neutron spectrum and xs
MCNP等方法给出而非
假设新的分割方法为
对能谱部分的转换为：

## Slide 17: How many bins of energy
Calculated the numerical integration of 329 (n, g) xs and neutron spectrum（111 energy points）
Distance to the result of 1e8 bins
Error is less than 0.1% with 1e6 bins
0.01-0.1 s computation time for each isotope
Computation time

## Slide 18: Calculation of Isomer ratio
Talys provides isomeric ratios of discrete energy points
Calculating weighted average isomeric ratio. The weight is neutron flux at the energy point
Output file of talys (part)
Weighted average
Input file of talys

## Slide 19: Weighted average，In-116 g & m & n
Notes: averageIR(matIR,neutronSpec)

## Slide 20: Sensitivity result
Irradiated in the 9 MeV new station，without Cd

## Slide 21: Branch ratio of the most intense gamma
How “clean” is the element decay gamma

## Slide 22: Comparation: Cyanus and experiment result
General Atomic Triga Mark I reactor（4.3e12 nv）
Irr=1h, cool=0,
Notes: In year 1965.

## Slide 24: 25.3 meV & Maxwell-Boltzmann

## Slide 25: TALYS的部分异常
Ti-47中子俘获后不应有Ti48m（NUBASE2020无）

## Slide 26: 中子活化法与PhotonAssay对比
PhotonAssay
完整评估了Au, Ag, Cu, Pb
粗略评估了15种核素
理论推测36种核素可测？
中子活化法有排他性优势：
Na, Mg, Al, V, Mn, Co, As, Nb, Rh
PhotonAssay的表有问题？
例如Cr怎么测

## Slide 27: PhotonAssay的检测能力表格可能有问题？
光核反应阈能
核素图局部
利用V52和V53可行，但是(gamma, p)阈能在11MeV以上，有较多的伴随粒子

## Slide 28: CYANUS development plan
2022.04.21. CYANUS_v1.0 内测
预计下版本优化：
  同质异能态问题的精细研究
  探测器伽马响应模块

## Slide 29: Memorandum
The majority of Zr97 delayed gamma comes from the decay of Nb97. Thus, the Cyanus result seems low.

## Slide 30
Thanks for your attention

## Slide 31
Thanks for your attention

## Slide 32: 内容提要
完善调研
  反射体选材
  各元素分析技术特点
  各中子源特点
理论分析
  样品要求（样品颗粒度等）
  双比较片原理与效果分析
  照射空间设计问题
缓发伽马能谱模拟程序
  元素含量，时间 对性能影响评估
  多反应道和衰变信息 对性能的影响
  能谱调制 对性能的影响
写作
  矿石的超热中子分析
  开题综述（调研与理论分析）
Notes: 特点：性能，适用范围

## Slide 33: 截面注量积分 int_evb的计算

## Slide 34: 缓发伽马模拟程序
元素质量构成表
table_element
核素构成表
table_isotope
同位素丰度
中子能谱
中子俘获截面
多同质异能态
衰变常数
无限照射活化表
table_decay
三时长
衰变常数
特定时间能点表
table_gamma
伽马能量
伽马分支比
模拟能谱
探测器单能响应
红色未完成

## Slide 35: 在9MeV优化位置照射1min，冷却1min
产生1cps特征伽马的质量下限
与MURR结果不算很好吻合，在同质异能态的处理上有区别（Y, Nb, Eu等）
仔细处理的In同质异能态吻合很好

## Slide 36: 实测谱 st851(20210627)
未考虑探测器响应（伽马自吸收，本征效率等）
按照559.1As高度相等对比两谱

## Slide 38: 缓发伽马模拟程序
丰度，半衰期，缓发伽马能量
  https://www-nds.iaea.org/pgaa/iaeapgaa.htm
  https://www-nds.iaea.org/pgaa/databases.htm
多同质异能态
  手工摘自论文
中子俘获截面
  ENDF-B 8.0 （使用NJOY处理为pointwise表）
缓发伽马能量和分支比
  ENDF-B 8.0 （正在研究如何解读）
其它
  自定：中子能谱，三时长

## Slide 39: 代码正确性验证
单能点纯核素伽马计数率正确
差别仅来自丰度、分支比等使用的数据库不同
Notes: 1g Au – 65000cps

## Slide 40: k0-IAEA程序可做比照？
k0-IAEA software is applicable only to a mostly thermal neutron flux
Installing and operating takes time

## Slide 41: 下一步工作
代码工作
  同质异能态问题
  交叉验证（如k0-IAEA program等）
  考虑探测器响应
实验
  7MeV 典型位置中子剂量率留档（3月11日，LB6411）
  9MeV 新靶实验（正在加工，预计3月底到位）
调研与写作
  《矿石的超热中子分析》
  根据开题报告意见逐条补充调研
  根据调研完成开题综述

## Slide 42
CYANUS的性能的交叉验证
2022年 11 月 19 日
崔桐源
矢车菊Centaurea cyanus
灰喜鹊 Cyanopica cyanus
喜鹊 Pica pica

## Slide 43: CYANUS的能力验证
四种方法计算4.3e12nv热中子照射1g任意核素，最强伽马射线强度
① Yule 反应堆实验
② CYANUS 直接计算
③ NIST 原始数据是活度，进一步计算强度
④ WISE 原始数据是活度，进一步计算强度
NIST
WISE

## Slide 44: Z=8-82共73个核素的初步情况
① WISE 没有考虑isomer（15个）：
Sc-46 Co-60 Se-81 Rb-88 Sr-89 Nb-94 Cd-117 In-114 Sn-121Cs-134 Eu-152 Dy-165 Er-171 Lu-177 Hf-181
② NIST 特殊（3个）：
Cr-55，Pr-142m（缺失），Ir-192m
③ Yule特殊（5个）：
Cu-64 Rh-104m Sn-125 Hg-199m Pb-207m
④ CYANUS特殊（1个）：
Sb-124m
⑤ 互不一致（3个）：
Kr Xe Os
⑥ cyanus和yule一致，另两个一致（7个）
Fe-59，
Zn-69m，
Ga-72,
Ge-75m,
Y-90m,
Pd-109m
Yb-177m
⑦ WISE 和实验一致，另两个一致（2个）
Gd-159
Re-188
⑧ cyanus和wise一致，另两个一致（1个）
Ta-182
3+1
2+2
1+1+1+1

## Slide 45: Z=8-82共73个核素的初步情况
小结：目前已基本确认WISE和NIST计算器都有不足之处，Cyanus在大多数核素的分析上是最准确的
下一步工作：① 明确WISE和NIST出现outlier情况的来源
②以下12个核素需更多资料佐证才能确定分析是否正确：

## Slide 46: Z=8-82共73个核素的初步情况
① WISE 没有考虑isomer（15个）：
Sc-46 Co-60 Se-81 Rb-88 Sr-89 Nb-94 Cd-117 In-114 Sn-121Cs-134 Eu-152 Dy-165 Er-171 Lu-177 Hf-181
② NIST 特殊（3个）：
Cr-55，Pr-142m（缺失），Ir-192m
③ Yule特殊（5个）：
Cu-64 Rh-104m Sn-125 Hg-199m Pb-207m
④ CYANUS特殊（1个）：
Sb-124m
⑤ 互不一致（3个）：
Kr Xe Os
⑥ cyanus和yule一致，另两个一致（7个）
Fe-59，
Zn-69m，
Ga-72,
Ge-75m,
Y-90m,
Pd-109m
Yb-177m
⑦ WISE 和实验一致，另两个一致（2个）
Gd-159
Re-188
⑧ cyanus和wise一致，另两个一致（1个）
Ta-182
3+1
2+2
1+1+1+1

## Slide 47
Thanks for your attention
Fight for the paper and thesis!

## Slide 48: ENAA有价值的核素
I, As, Au, Cd, Ni, Se, Br, Rb, Sr, Mo, Sb, Ba, Ta, Th and U
Ismail. Shaaban, “Design of a permanent epithermal neutron irradiation site in the Syrian MNSR,” Progress in Nuclear Energy, vol. 52, no. 6, pp. 569–572, Aug. 2010, doi: 10.1016/j.pnucene.2010.01.008.
X. Hou, K. Wang, and C. Chai, “Epithermal neutron activation analysis and its application in the Miniature Neutron Source Reactor,” Journal of Radioanalytical and Nuclear Chemistry Articles, vol. 210, no. 1, pp. 137–148, Oct. 1996, doi: 10.1007/BF02055413.